## Slide 1
MC2101: A RISC-V-based Microcontroller for Security Assessment and Training
Author: Luca DALMASSO
Advisor: Paolo Ernesto PRINETTO
Co-Advisor: Gianluca ROASCIO
Notes: design of MC2101:
work realized under the supervision of P. and R.

## Slide 2: License & Disclaimer
This presentation is licensed under the Creative Commons BY-NC License
To view a copy of the license, visit:
http://creativecommons.org/licenses/by-nc/3.0/legalcode
We disclaim any warranties or representations as to the accuracy or completeness of this material.
Materials are provided “as is” without warranty of any kind, either express or implied, including without limitation, warranties of merchantability, fitness for a particular purpose, and non-infringement.
Under no circumstances shall we be liable for any loss, damage, liability or expense incurred or suffered which is claimed to have resulted from use of this material.
License Information
Disclaimer

## Slide 3: Outline
Introduction
MC2101 Microcontroller
  Architecture
  Peripherals
Experimental Results
Conclusions
Notes: introduction on the context in which the present work is involved
purposes of this thesis work
overview of the main components and functionalities the designed platform can provide
In the experimental results are discussed and reported the resources used by this platform once synthesized on FPGA
Conclusions

## Slide 4: Introduction
Embedded systems are massively used as edge devices in:
  Safety-critical applications
    Cars, Aircrafts, Trains, Medical equipment, …
  Business-critical missions
    Industrial automation, telecommunications, …
Key benefits:
  Real-time reliable
  Low manufacturing cost
  Low power consumption
  Require minimal human intervention on the field
Notes: They play crucial role in functioning of cars, aircraft, trains, medical equipment
Real time reliable
engineered to solve very specific tasks with no or little delay
guaranteeing at the same time low power consumption and low manufacturing cost

## Slide 5: Introduction
Such devices must be secure and reliable
Problem:
  Built-in device security is minimal
Research Solution:
  Software-based techniques
    Can be easily tested outside the operating environment with a proper software toolchain
  Hardware-based solutions
    Require a CPU architecture description to be physically tested
      Most famous architectures are licensed (Intel, ARM) and not accessible to research
      Production of new silicon (e.g., ASIC) is unaffordable
Notes: safety/business-critical missions require secure and reliable devices
The problem : Being cheap and low power imply being constrained in terms resources and performances (few KB of Memory, Few MHz CORE that are not enough to support robust HW and OS)
CONSEQUENCE: build in device security is minimal
SOLUTIONS
software: protect the system at app level
hardware: protect the system at hard level
Hardware solutions require real hardware to be tested and evaluated --> because most popular architecture in use (x86, ARM) are licenced and not accessible, research and academia need an open architecture

## Slide 6: Introduction
To evaluate both HW/SW security solutions
Open-source design
customizable starting from the core itself
Open-source ISA
Simple
Supported by popular software toolchain, e.g., GNU GCC
RISC-V ISA
Synthesizable on FPGA
Notes: To evaluate HW/SW solutions: research community needs an architecture that UNLIKE Intel or ARM is fully accessible
Among all the known open source designs, the most complete is the RISC-V ISA

## Slide 7: Introduction
Simple
Small standard base (47 instructions)
Modular ISA
Additions via optional extensions
Designed for Extensibility
Stable
Base is frozen
Today's open-source standard in embedded systems design
Notes: 47 instructions are enough to build a minimalistic RISC-V machine

## Slide 8: Introduction
Purpose of the thesis work: design MC2101, a modular, extensible and synthesizable embedded system to be used as a reliable platform for:
  Integrate and evaluate security solutions for embedded/IoT domain
  Run real applications
  Teaching microcontrollers architecture
  Security training activities for students and professionals
    E.g., Capture-the-Flag challenges

## Slide 9: MC2101 Architecture: overview
The microcontroller includes:
  A 32-bit RISC-V processor: AFTAB
    Designed at PoliTO and developed by University of Tehran
    Sequential core
    RV32IM Subset RISC-V ISA
      Integer base + Multiplication and Division Extension
      Subset of privilege extension for interrupts and exceptions
    Master of the BUS
    Access peripherals and RAM in memory mapped mode.

## Slide 10: MC2101 Architecture: overview
Single BUS interconnecting the processor with memory and peripherals
  Supports multi-cycle R/W operations
  Control signals for interrupts
  Control signals for transfer response
Minimal set of peripherals designed to provide all necessary I/O functions
  GPIO, UART

## Slide 11: MC2101 Architecture: GPIO
General Purpose Input Output (GPIO) peripheral
  Present in every microcontroller
  Designed to manage incoming and outcoming digital signals
    Controlling physical pins
    Bit-banging operations
The logic and the software library designed allow to:
  configure pins direction
  read/write pins logic state
  enable interrupt on each input pin
  configure interrupt triggering behavior
Notes: present in every microcontroller because it can be used for a diverse variety of applications.
physical pins --> in FPGAs can be mapped to a lot of components like BUTTONs, LEDs, SWITCHEs

## Slide 12: MC2101 Architecture: UART
The UART module designed for MC2101 provides a receiver-transmitter pair
  Configurable with different speeds
  Supporting different data widths
  Parity codifications
  Information status for different error conditions:
    Overrun Error, Frame Error, Break Interrupt
  Prioritized interrupts
  Buffered communications
    Two dedicated hardware FIFO’s
Notes: error conditions and parity allow to monitor the integrity of a communication
buffered communications for optimizing interrupts triggering and transmissions

## Slide 13: MC2101 Architecture: UART
Communication channel between PC and the microcontroller synthesized on FPGA
  Uart Tx and Rx are bridged to USB
  Through a PC terminal, it is possible to send/receive characters
    Software libraries integrate scanf & printf functions
Notes: the software also include string manipulation functions togheter with the printf and scanf.

## Slide 14: Experimental Results
Synthesized on Cyclone-V FPGA using Quartus 21.1 software
Very small percentage of available resources is used
  Great deal of freedom for future developments
Resource Name | Used Amount | Total Amount | Percentage Used
ALM | 2628 | 32070 | 8%
FF | 3443 | 64140 | 5%
PIN | 36 | 457 | 8%
M10K Memory Bits | 131072 | 4065280 | 3%
M10K Blocks | 16 | 397 | 4%

## Slide 15: Conclusions
Creation of a fully synthesizable design
Architecture and software libraries allow MC2101 to be used on a development board
Tests demonstrated the ability of the system to perform all the functions setup
Included software toolchain allows to automate synthesis processes, RTL simulations, and compilation of custom applications
Notes: software toolchain based on CMake and Make tools, ModelSim and Quartus commands that together allow the automation

## Slide 16
Thanks for your attention!